## Slide 1
  Mitigations
RIDL Rogue In-Flight Data Load
  Attacks
  Behaveour
https://mdsattacks.com/

## Slide 2
Microarchitectural Data Sampling
Side-channel vulnerabilities in Intel CPUs
private data can leak across arbitrary security boundaries
Attackers can inspect µ-architectural buffers
https://mdsattacks.com/

## Slide 3: µ-architectural (shared) buffers
It's possbile to discover and analyze the behaveour of µ-architectural buffers via reverse engineering
Performance counters:
Cache and buffers hits
µ-architectural requests
Speculative loads (Spectre):
FLUSH+RELOAD
PRIME + PROBE
CrossTalk: Speculative Data Leaks Across Cores Are Real. Ragab, H.; Milburn, A.; Razavi, K.; Bos, H.; and Giuffrida, C. In S&P, May 2021. Intel Bounty Reward

## Slide 4: Listen the "noise" from another thread
S. van Schaik et al., "RIDL: Rogue In-Flight Data Load," 2019 IEEE Symposium on Security and Privacy (SP), San Francisco, CA, USA, 2019, pp. 88-105, doi: 10.1109/SP.2019.00087.

## Slide 5: Line Fill Buffer
S. van Schaik et al., "RIDL: Rogue In-Flight Data Load," 2019 IEEE Symposium on Security and Privacy (SP), San Francisco, CA, USA, 2019, pp. 88-105, doi: 10.1109/SP.2019.00087.
µ-optimization:
Non-blocking cache
Load squashing
Write combining
Non-temporal requests
Reads that are not served from L1d pull data through the LFB, while writes push data through the LFB to either L1d or memory

## Slide 6: Synchronization
To leak information, the attacker must make sure that the right data is visible in the LFB at the right time, by synchronizing with the victim. This can be done in 3 different ways:
Serialization
mfence instruction guarantees that both load and stores before it's execution become globally visible (eg in the LFB).
The mfence instruction forms a point of synchronization that allows us to observe the last few loads and stores before the buffers are completely drained.
Contention
With victim and attacker running in the same hardware thread (e.g., in a sandbox, without SMT), we can create contention forcing entries to be evicted from the LFB.
Eviction
We can control the values that we leak from the victim by evicting cache entries from the cache set in which we are interested. If these cache lines were dirty, the processor has to write them back through the memory hierarchy and will do this through the LFB.

## Slide 7: CrossTalk
CrossTalk: Speculative Data Leaks Across Cores Are Real. Ragab, H.; Milburn, A.; Razavi, K.; Bos, H.; and Giuffrida, C. In S&P, May 2021. Intel Bounty Reward
Exploiting RIDL capabilities of reading µ-architectural buffers It's possible to leak the deep impementation of instructions
CPUID RDRANDR RDSEED CLFLUSH RDMSR
We are intrested in:
OFFCORE_REQUESTS
OFFCORE_RESPONSE
buffers flush

## Slide 8: CrossTalk: The shared buffer
CrossTalk: Speculative Data Leaks Across Cores Are Real. Ragab, H.; Milburn, A.; Razavi, K.; Bos, H.; and Giuffrida, C. In S&P, May 2021. Intel Bounty Reward
The Staging Buffer is Shared among all cores
The Staging Buffer is used to store pending request to unique (shared) resources like the Random Number Generator; for optimization purpose this buffer is able to aggregate
µ-operations delivering unrequested data to ALL cores LFB
Note that the interconnection mechanis is (probably) asincronous

## Slide 9: CrossTalk (in action)
CrossTalk: Speculative Data Leaks Across Cores Are Real. Ragab, H.; Milburn, A.; Razavi, K.; Bos, H.; and Giuffrida, C. In S&P, May 2021. Intel Bounty Reward